## Slide 1: Linwood Place Spring general meeting
Rain barrels
By Craig miller

## Slide 2: Rain barrels and water collection
1 inch of rain on 1000 sq ft of roof will net 600 gallons of water
Ideal for watering indoor/outdoor plants
Lessens the amount of storm runoff in the streets
Can also be used to collect the condensate from your Air conditioning system

## Slide 3: Things to consider
Rain barrel location
  Away from basements, unless adequate overflow system is created
  Out of sight?
Orientation
  Bank of rain barrels
  Single rain barrel under a downspout
Placement
  On the ground
  elevated

## Slide 4: Supplies (barrels)
Where to get rain barrels in OKC
  Craigslist
    Least expensive ~$20-40 per barrel
    Require more work, setup is diy
  Upcycle products
    Cost is slightly higher @ $64 per barrel
    Barrels come with all hardware attached
    Multiple color selections
    Orders are placed through the company and picked up at the public works on s. Portland
      Online order deadline is June 12th

## Slide 5: Supplies (hardware)
Downspout diverter
Spigot
Overflow
Linking hoses (for barrel banks)
Mesh screen for debris and mosquito control
Barrel conversion kits

## Slide 6: Supplies (tools)
Drill
Hole saw
Channel lock pliers
Small hand saw
  For barrels with permanently fixed lids

## Slide 7: Assembly
Overall assembly will vary greatly based upon hardware selected
Elevate the spigot enough to be able to attach a hose
  Around 6” for barrels that are on the ground
  As low as achievable for barrels that are elevated
Carefully consider the location of the ports for linking systems
  Better If linked at the bottom
    the barrels have more time to level during a downpour
    Only one spigot needed for draining the barrels

## Slide 8: Mosquito control
Mosquitoes will breed in the rain barrels if they are not adequately protected
Mosquito control options
  Screens
    Set it and forget it
    Easy to build
  BTI
    A bacteria that is put into the water and only kills mosquitoes, gnats, and blackflies
    Comes in multiple forms (liquid, granules, or dunks)
    Must reapply according to manufacturer’s recommendations
  Fish
    Goldfish, guppies, and mosquito fish are all known for eating mosquito larva
    Must supplement their diet in non-mosquito season and provide a place for them to live in the winter
    Rain barrel must be out of the sun, as the temperature of the water can become too warm

## Slide 9: Resources
Upcycle products :
  http://www.upcycle-products.com/static.asp?path=6216
Okc utilities department water conservation website:
  http://squeezeeverydrop.com/Home.aspx
  Rain barrel tutorial:
    http://squeezeeverydrop.com/SavingWaterOutdoors/RainBarrels.aspx
Brass hardware specifically for rain barrels
  http://www.amazon.com/s/ref=nb_sb_noss_1?url=search-alias%3Dlawngarden&field-keywords=rainpro